AcouSed general layout with physical dependencies of inversion method for high concentration
Sediment calibration data
Input data for acoustic inversion
Instruments
Frequencies
Backscatter signals
Sample for calibration
PSD for calibration
Fines profile
Temperature
alignl size 16 stack{k_{t ref} ~ ~ ~ ~ ~ size 12 {[V.m^{3/2}]} # %nu_i ~ ~ ~ ~ ~ ~ ~ size 10 {[Hz]} # V_{BS}^{sed},`V_{noise}^{sed} ~ [V] # M^{sed}_{sand} ~ ~ ~ size 12 {[kg.m^{-3}]} # n(a_{s}) # M^{sed}_{fine}(r) # T_{sed} ~ ~ ~ ~ ~ size 10 {[°C]} }
Position x or t
Calibration
Model parameters
alignl size 12 {stack{k_{t, i} = k_{t, i}(k_{t ref}, ` %nu) ~ ~ ~ ~ ~ ~ ~ [V.m^{3/2}] # %zeta_i = %zeta_i(%nu, ` n(a_s)) ~ ~ ~ ~ ~ ~ [m^{2}.kg^{-1}] # X_i = X_i(%nu, ` n(a_s)) } }
Vertical
Recording : Section = depth vs distance from bank
       Single position = depth vs time
Output data
Acoustic inversion
Acoustic data
Signal pre-processing
Averaged and filtered signal
Model
Backscatter signal
alignl size 18 { binom{SSC_{sand} ~ [kg.m^{-3}]}{SSC_{fine} ~ [kg.m^{-3}]} }
alignl size 16 binom{V_{BS}(%nu) ` [V]}{T[°C]}
alignl size 18 color blue {{VBI ~ [s^{X}.m^{-1}]}}
size 20 {overline V_{BS}, ` SNR size12 {(V_{BS}, V_{noise})}}
Input sample(s) data for comparison / validation
Sample data
size 16 {M^{val}_{sand}, M^{val}_{fine}}
Backscatter signal to compute SNR
size 20 {V_{noise} ` [V] }
Depth

---
AcouSed general layout with Signal/Noise Ratio (SNR) details
alignl size 16 stack{k_{t ref} ~ ~ ~ ~ ~ size 12 {[V.m^{3/2}]} # %nu_i ~ ~ ~ ~ ~ ~ ~ size 10 {[Hz]} # V_{BS}^{sed},`V_{noise}^{sed} ~ [V] # M^{sed}_{sand} ~ ~ ~ size 12 {[kg.m^{-3}]} # n(a_{s}) # M^{sed}_{fine}(r) # T_{sed} ~ ~ ~ ~ ~ size 10 {[°C]} }
alignl size 12 {stack{k_{t, i} = k_{t, i}(k_{t ref}, ` %nu) ~ ~ ~ ~ ~ ~ ~ [V.m^{3/2}] # %zeta_i = %zeta_i(%nu, ` n(a_s)) ~ ~ ~ ~ ~ ~ [m^{2}.kg^{-1}] # X_i = X_i(%nu, ` n(a_s)) } }
Input VBS for
acoustic inversion
alignl size 16 {SNR(%nu) = frac { alignc (overline V_{BS} - V_{noise})^2} { alignc (V_{noise})^2}}
Measured / Profile tail / Value

---
AcouSed general layout with sediments calibration details
alignl size 12 form function : f_{infinity} = f_{infinity}(T, ` %nu_i, ` a_s) ` + ` sand PSD : n(a_s)
alignl size 12 {size 18 bold {k_t} = k_{t ref}} sqrt{frac {alignc %tau(T_{sed}, %nu) c} {alignc %tau_{ref} c_ref}}
alignl size 12 c(T_{sed})
[m.s-1]
alignl size 16 stack{k_{t ref} ~ ~ ~ ~ ~ size 12 {[V.m^{3/2}]} # %nu_i ~ ~ ~ ~ ~ ~ ~ size 10 {[Hz]} # V_{BS}^{sed},`V_{noise}^{sed} ~ [V] # M^{sed}_{sand} ~ ~ ~ size 12 {[kg.m^{-3}]} # n(a_{s}) # M^{sed}_{fine}(r) # T_{sed} ~ ~ ~ ~ ~ size 10 {[°C]} }
[V.m3/2]
alignl size 12 k_{s} = left[ frac { int from{0} to{ infinity } a_s^2 f_{infinity}^{2}(a_s)n(a_s)da_s } { %rho_s int from{0} to{infinity} a_s^3 n(a_s) da_s } right] ^{1/2}
alignl size 12 J^{sed} = frac {alignc 3} {alignc 16%pi} frac {alignc overline {(V_{BS}^{sed})^2} r_{s}^{2}} {alignc k_{t}^2 }
alignl size 12 s_{v} = frac {alignc 3} {alignc 16%pi} k_{s}^{2} M^{sed}_{sand}
[m-1]
[m-1]
[m.kg-1/2]
alignl size 12 %alpha_{s} = {frac {alignc log( s_{v} / J^sed ) } {alignc 4r_{s} }} - %alpha_{%omega}
alignl size 12 %alpha_{%omega}(T_{sed}, %nu_i)
[m-1]
[m-1]
alignl size 12 {size 18 bold {X}} = left( frac {alignc log( s_{v,i} / s_{v,j} ) } {alignc log( ital %nu_i / ital %nu_j ) } right) _{( i <> j )}
alignl size 12 {size 18 bold {%zeta}} = {frac {alignc %alpha_s } {alignc frac {1} {r_{s}} int from{0} to{r_{s}} M^{sed}_{fine}(r)dr }}
[m2.kg-1]
alignl size 18 color blue {VBI ~ [s^{X}.m^{-1}]}
size 16 {M^{sed}_{sand}, M^{sed}_{fine}}

---
AcouSed general layout with inversion calibration details
Input data for method calibration
alignl size 18 stack {k_{t,1} ` , ` k_{t,2} # %zeta_1 ` , ` %zeta_2 # X }
alignl size 14 stack{V_{BS}^{sed} ~ [V] # M^{sed}_{sand} ` size 10 {[kg.m^{-3}]} # n(a_{s}) # M^{sed}_{fine}(r) # %nu_i ~ size 10 [{Hz}] }
alignl size 16 color blue {binom {log(VBI) = {alignc %zeta_{2}log(J_{1} e^{(4r %alpha_{ %omega, 1})} / %nu_{1}^{X}) - %zeta_{1}log(J_{2} e^{(4r %alpha_{ %omega, 2})} / %nu_{2}^{X} )} over {alignc %zeta_{2} - %zeta_{1}}} {(%nu_1, ` %nu_2), ~ (J_1, ` J_2), ~ (%alpha_{%omega_1}, ` %alpha_{%omega_2}) }}
size 20 {overline V_{BS}, ` SNR size12 {(V_{BS}, V_{BS}^{noise})}}
size 18 {V_{BS}^{noise} ` [V] }
alignl size 14 { binom{SSC_{sand} = {alignc 16%pi × VBI × {%nu}_{2} ^ {X}} over {alignc 3 {k} rsub {s} rsup {2}} } {SSC_{fine} = {1} over {%zeta_2} left [{alignc 1} over {alignc 4r} log {left ({alignc VBI × {%nu}_{2} ^ {X}} over {alignc J_2} right ) − {%alpha} rsub {%omega}} right ]} }