7
2
1
3
5
4
6

---
Step 1
Select AQUAscat
Step 2
Click on green cross button and select file 20240703111300.aqa
Step 3
Select AQUAscat Romanche 2024
Step 4
Set the temperature to 10°C and press Enter
Step 5
Set the upper limit to 350 sec and press green arrow button (on the same line)
Step 6
Select 0,3 MHz and set -0,8 m and -0,5 m for, respectively, the interval start and end of the first interrogation area.
Set 0,01 m for the next interrogation area gap
Step 7
File → Export → Table of Backscatter values
Select a folder. Data are record in a csv file with the default name Table_20240703111300.csv (Table_*acoustic file name*.csv)

---
4
6
5
4

---
Click on blue refresh button
Select Profile tail method
Set the noise value to 0,006 Volts and click on green arrow button
Step 4
Set the SNR to 0 and press green arrow button (optional - for this case, inversion works well without filtering with SNR)
Step 5
Set the number of profile to ±160 cells and press enter. This number is converted to time in seconds.
Step 6
Click on red arrow button to compute average and to update plots.

---
Click on Plot Acoustic data button
Click on folder button and select file fine_sample.ods
Click on folder button and select file sand_sample.ods

---
5
7
4
6
8

---
Click on blue refresh button
Select 0,3MHz for the Frequency 1 and 1MHz for the Frequency 2
Select F11, F12 and F13 for Fine profile
Select S11 for Sand target
Step 4
Click on Plot sample button to plot the samples concentrations profile
Step 5
Click on Interpolate button to interpolate the profile
Step 6
Select Compute sediment calibration and click on Compute Calibration
Step 7
Click on OK to close the validation window
Step 8
Click on Save Calibration and select the folder. The calibration data is record in a file with tha default name Sediment_calibration_20240703111300.csv (Sediment_calibration_*acoustic file name*.csv)

---
9
5
4
6
8
7

---
Click on blue refresh buton
Click on RUN INVERSION button
Set profile to 300 and press Enter to plot the fine concentration profile at the sample position (you can use the figure toolbar to adjust plot limits)
Step 4
Select F11 and F12
Step 5
Click on blue refresh button to refresh the plot Measured SSC fine vs Inverted SSC fine
Step 6
Set profile to 300 and press Enter to plot the sand concentration profile at the sample position (you can use the figure toolbar to adjust plot limits)
Step 7
Select S11 and S12
Step 8
Click on blue refresh button to refresh the plot Measured SSC sand vs Inverted SSC sand
Step 9
Click on Save results button. Choose the directory and set filename of the csv or xlsx file.